INFORMATION on DIGITAL CLOCK held by CHESHIRE COUNTY AA

(Please note that the digital clock + its cover, battery and battery charger are the property of the Northern Athletics and is held by Cheshire County AA).

Details :

- The clock is a double-sided large 6 digit display (format hh:mm:ss) and requires a 12v dc battery to operate.  A battery and charger are available, but the clock will operate satisfactorily from a car battery.

- Dimensions : 131cm long, 25cm wide, 42cm high, weight 28kg (about 60 lbs).  (This is slightly larger and heavier than the double sided clock available through Greater Manchester AA)

- The base of its frame extends to the full length, providing a means to fit to a roof rack or roof bars, but note the weight of the clock.  The connecting cable is sufficiently long for the battery to be on the floor of most vehicles.

Operating Instructions :

(also on the control box)

- Connect clock to battery observing the correct polarity.

- Plug separate control box into one end of the clock case via lead provided.

3. TO START :

a) Press “SET HRS” and “SET MINS” buttons (black) on control box together to reset internal clock.

- Press “RESET” button (red) to clear display.

[If START button (Green) is now pressed the clock will start from zero display

OR TO START from a PRESET TIME,  carry out a) and b) above, then set required HRS and/or MINS by pressing appropriate buttons which advance time by one digit per press.

c) Press “START”

4. To stop the clock, press “HRS” and “MINS” buttons simultaneously - the clock will then hold and display the stop time.

- To clear the display, press “RESET” button.  (Note that the display clears   sequentially in steps taking a couple of seconds in total - this reduces the drain on the battery in comparison with older models in which all digits cleared at the same time).

Note also, that when the clock is operating and a major change of time takes place (e.g. from 00:59:59 to 01:00:00) the digits change sequentially, not simultaneously).

Northern Athletics owned digital clocks are also stored in :

Greater Manchester (double sided) - contact : Arnold Bradshaw (Tel : 0161  796 6310)

Merseyside (single sided) - contact : Mike Dooling (Tel : 0151 289 8082)

John Driscoll

2 September 2006/25 April 2007.